## Slide 1
CEC – 1434 / CEC – XXXX
Advanced Corridor Modeling Using Trimble Business Center

## Slide 2
CEC – 1434 / CEC – XXXX
Advanced Corridor Modeling Using Trimble Business Center
Alan Sharp
Business Area Director – CEC Software

## Slide 3: Abstract
This session will take a deep dive into Trimble Business Center road and corridor modeling tools, and demonstrate advanced use cases and concepts.
Have you ever wondered
  How Conditional Instructions can be used?
  How to start and stop template elements at specific stations
  How to measure surface areas as well as material volumes in a Corridor Earthworks Report?
  How to model MSE Walls and structural / non structural excavation quantities?
All of these questions and more will be addressed with practical use cases.
There will also be time for advanced question and answers so come prepared with your model building or takeoff questions

## Slide 4: Learning Objectives
Use Conditional Template Instructions within a corridor model
Model over-excavation areas for a corridor model
Increase productivity with advanced corridor modeling skills

## Slide 5: Quick Question As A Starting Point
Who in the room is new to Business Center – HCE / Trimble Business Center Corridor modeling?

## Slide 6
Let’s Get Going

## Slide 7
The Use Of ? (Undefined) and Previous and Specific Node in Template Instruction Tables

## Slide 8: Reference Node Use Cases
Previous Node
Shape will always be created – connected to the last node that was created
Previous Node may vary along the corridor depending on the template
May not always give you what you wanted!
Specific Node
Shape will only be created where the specified node was created before it
Node may stop and start along the corridor depending on the template
Can be used to define groups of shapes that go together (start and stop together) based on a specific seed node in the template

## Slide 9: Using Tables for Offsets, Slopes and Elevations
12’ @ -2%
12’ @ -2%
12’ @ -2%
12’ @ -2%
0+00
0+50
1+30
2+30
2+80
3+80
4+60
5+10
HAL
EOPR
TAPR
TAPR
Stop TAPR Here
Restart TAPR Here
Start TAPR Here
End TAPR Here

## Slide 10: Offset and Slope Tables
Station | EOPR |  | TAPR | 
 | Offset | Slope | Offset | Slope
0 | 12 | -2 |  | 
50 |  |  | 0 | -2
130 |  |  | 12 | -2
230 |  |  | ? | ?
280 |  |  | 12 | -2
380 |  |  | 12 | -2
460 |  |  | 0 | -2
460.01 |  |  | ? | ?
510 |  |  |  | 
? Stops the node from here forwards
? Stops the TAPR node from here forwards
Note: Cannot Taper and Stop with a ?
Tapers TAPR to 0 width
Choose your method – I use .01 beyond the defined Station in most cases. You could also do 459.99 and 460.00 so that it is stopped by the defined Station

## Slide 11
Let’s Take a Look At An Example Road Model With This Setup

## Slide 12
Conditional Instructions
How and When To Use Them

## Slide 13: Conditional Instructions
Scenario 1 – One or Two outcomes
If
  True Condition Instructions
Else
  False Condition Instructions
End
Note:
You can do only the True condition and then End. If the test condition fails then nothing happens
Scenario 2 – Multiple Outcomes
If
  True Condition Instructions
Else If
  Another set of True Condition Instructions
Else If
  Another set of True Condition Instructions
….
Else
  Final Fail Condition Instructions (catch all)
End
Note:
Else If statements keep executing until one passes – when one passes, it’s instructions are executed and all other Else Ifs and Else statements are skipped and the If set terminates
If Statements Can Be Nested For Complex Scenarios

## Slide 14: Conditional Tests Supported
Node is above surface
  Conditional Fill side slope
Node is below surface
  Conditional Cut side slope
Node’s vertical offset from surface
  Conditional side slope based on depth of cut or fill or a strata check e.g. for Rock
Node’s distance from node
  Haven’t found a use for this one yet ….
Node’s horizontal distance from node
  Test to see if the Test Node is inside or outside the ROW line
Node’s vertical distance from node
  Could be used to decide “side slope” or “retaining wall” for example

## Slide 15: Conditional Instructions
The key to conditional statements is the creation of the Condition – how do you establish a suitable condition?
You will often need to create a “Test Shot” that is not assigned to a Material Layer that you can then use to do the test.

## Slide 16: Condition Example
ROW
3:1
4:1
Test Shot
HAL
EOP
FSR
Is the Test Shot inside the ROW line?
If Yes then do a 3’ Ditch and a 4:1 slope
If No then do a 3’ Ditch and a 3:1 slope

## Slide 17: How To Set Up The Test
Change the elevation of the ROW line to that of the Existing Ground Surface
Add the ROW line to the Corridor as a Reference Line
From Point FSR create a Cut Side Slope with the 3’ Ditch width and the 4:1 Cut Slope to Existing Ground. Leave all Material Layers unchecked. Call the Tie Point “Test ROW Point Right”.
This will be your test point

## Slide 18: Setting up the Condition
The order you pick the Test Node and the Node 2 dictates the “sign” of the values being tested
I stated if ROW Test Point is Inside the ROW line
ROW Node – Test Node = +ve value = Pass condition (>=0 <10000) range
Tip - When you create an If also create an End and then insert the Else / Else If and other template instructions in between

## Slide 19: OK – So We Setup for a 4:1 or 3:1 Slope
What happens when that fails ….
We do more tests to see what passes
  If 3’ Ditch and 4:1 Slope
  Else If 3’ Ditch and 3:1 Slope
  Else If 3’ Ditch and 2:1 Slope
  Else 3’ Ditch and 1:1 Slope (Catch All Condition – will show where the slopes cannot work)
  In some examples the side slope varies and then the ditch width varies to zero before the Catch All.
  Ideally the design has the Tie Slope from the Engineer and you can create a simple instruction that connects the Ditch and Tie Point and you don’t have to do the “Engineering” yourself (but this is common).

## Slide 20: Other Times When Conditions Will Help
If In Rock then …..
If Inside / Outside ROW then ….
If in Cut then …. / If in Fill then ….
Varied Tie Slope Conditions based on different situation conditions

## Slide 21
Modeling Over Excavation Conditions

## Slide 22: Over Excavation Conditions
Non Structural
Fill
Non Structural
Fill
Structural FIll
Finished Grade
Subgrade
Existing Ground
OverEx
OverEx
Non Structural Fill
Non Structural Fill
In Trimble Business Center – Existing Grade, Finished Grade and Subgrade is Pretty Clear and Obvious – but how do you tackle Overexcavation Surfaces. The trick here is to ensure that your Overexcavation Surface has to be 100% below Finished Grade model – so how do we model Finished Grade to achieve this?

## Slide 23: Building out the Finished Grade Surface
Surface Tie to EG
Surface Tie to EG
Surface Instruction use EG
Surface Instruction use EG
Surface Tie to EG
Offset / Slope
Offset / Slope

## Slide 24: Building out the Over – Excavation Surface(s)
Offset / Elevation
Offset / Elevation
Offset / Elevation
Side Slope
Side Slope
Offset / Elevation
Slope / Slope
Slope / Slope
Material Above
NSF
Material Above
NSF
Material Above
SF

## Slide 25
Let’s Take A Look At This Example Road Template

## Slide 26: Other Neat Tips in This Example
Coordinate Scroll
  End Section Areas and Materials Applied
Material Above Trick
  Default Subgrade Issue at Station ~1146.70
  Change Material Above 2 center Overex sections to Undefined to correct problem
Define Surface Areas in the Template
  MSE Wall Surface Areas
  Overex Surface Areas
Corridor Surface Model – To Show MSE Wall Areas
Surface Instruction – From and To Node – Explain how that works for the two EG Surface Instructions
0.8 x MSE Wall Height defines the Width of the excavation – How to solve for that

## Slide 27: Summary
Hopefully in this session you will have learned a number of “new methods” to model some of the more complex scenarios in road construction
The TBC Road Calculation engine is tremendously powerful, and can help you to compute many complex scenarios
Use the TBC engine to compute volumes and surface areas for estimating purposes and to build models for machine control / site positioning purposes

## Slide 28
How To Learn More In Future
Trimble Community Forum & Trimble Library

## Slide 29: Helping Yourself
Join the Trimble Library
  Free and Low Cost Video Library of Training Materials
  From a few $$$ to $50 for an entire training course
Join the Trimble Business Center Community Forum
  Free downloads of Project templates, Drafting Templates
  Free Support and Advice
  Give us your product improvement ideas
  www.Community.Trimble.com

## Slide 30
Questions?
Thank You
alan_sharp@trimble.com